## Slide 1
YOUR WAY
CREATING THE FUTURE
www.viettel.com.vn

## Slide 2
GIẢI PHÁP XÂY DỰNG MÔI TRƯỜNG VĂN HÓA GẮN KẾT, SÁNG TẠO GÓP PHẦN GÌN GIỮ VÀ THU HÚT NGUỒN NHÂN LỰC TRẺ CHẤT LƯỢNG CAO
THAM LUẬN
Đại hội Đoàn TNCS HCM Tập đoàn Công nghiệp Viễn thông Quân đội lần thứ VI
Khóa học chuyên đề
Phát triển giao thức mạng 5G
Hà Nội 08/2024
high tech

## Slide 3: Course

## Slide 4: Summary – Session 1
I. 5G Introduction
II. 5G Protocol Stack
III. Paging call flow and feature
IV. Mini-project

## Slide 5
I. 5G Introduction

## Slide 6: I. 5G Introduction
1. 5G
2. ITU
3. 3GPP
4. Network Architecture Overview
5. 4G/5G Non-standalone Architecture (NSA)
6. 5G Standalone Architecture (SA)
7. 5G in Vietnam

## Slide 7: 1. 5G
Object
  EMBB
  URLLC
  Mass type connections
Network Elements
  UE,
  Radio Access Network
  Transport Network
  Core Network
Key Technology ?
  Massive MIMO
  Beamforming
  Network slicing
  Network flexibility – Virtualization

## Slide 8: 2. ITU – International Telecommunication Union
ITU
  Founded 1985
  Agency of United Nation (UN)
  193 member states + 900 companies, universities and organization
  Coordinates the global use of the radio spectrum and defines requirements for next-generation mobile communication technologies.
3 main sectors
  ITU-R Radio Communication
  ITU-T Standardization (called Recommendation)
  ITU-D Development
Committed to connecting the world
Output document
  IMT-2000: define “3G”; year of release: 2000
  IMT-Advanced: define “4G”; year of release: 2010
  IMT-2020: define “5G”; year of release 2020

## Slide 9: 3. 3GPP – 3rd Generation Partnership Project
3GPP
  1998
  Is an standard organization
  From 7 regional organization partners (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC) + 700 companies
  Create & maintain technical standard for global mobile communication technologies as GSM, UMTS, LTE, NR
3 main group
  Radio Access Network
  Service & System Aspects
  Core Network & Terminal
Output document
  Release 99: “3G” UMTS standard
  Release 8: “first 4G” LTE standard; year of release: 2008
  Release 15: “first 5G”; NR standard; year of release: 2018

## Slide 10: 4. 4G/5G Network Architecture Overview
4G LTE option 1
4G/5G NSA option 3
5G SA option 2
https://www.digi.com

## Slide 11: 5. Non-standalone Architecture (NSA)
NSA option 3
Radio access network is composed of
  4G eNodeB as master node
  5G gNodeB as secondary node
Core is 4G core
Advance
  Quickly deploy
  Add only 5G gNodeB
  Increase throughput
Dis-advance
  Adapt only MBB
  Complex operation

## Slide 12: 6. 5G Standalone Architecture (SA)
SA option 2
Radio Access Network
  5G gNodeB
Core Network:
  5G Core
Advance
  Full 5G technology to achieve: MBB, ULLC, Mass types of connection
  Simple operation:

## Slide 13: Student work
Why 5G throughput is higher than 4G throughput ?
Calculation the peak 5G throughput

## Slide 14: 8. 5G in Vietnam
Viettel 5G trail spectrum license :
  Deploy 5g service 63/63 provinces
  NSA mode
5G spectrum license for 15 year
  Viettel: 2500-2600 MHz ; March 2024
  VNPT: 3700-3800; April 2024
Big 4G/5G vendor
  Ericsson
  Nokia
  VHT ( Viettel High Tech)
VHT exported 5G Private Network to India in August 2023

## Slide 15
II. 5G Protocol Stacks –
overview

## Slide 16: II. 5G Protocol Stack - gNodeB
1. Definition
2. gNodeB Interface
3. gNodeB Protocol Stack – Control Plane
4. gNodeB Protocol Stack – User Plane
5. 5G NR Layer 3
6. 5G NR Layer 2
7. 5G NR Layer 1

## Slide 17: 5G gNB Viettel
Chỉ tiêu kỹ thuật:
  Dung lượng: 3600 user/gNB
  Băng tần: 2496-2690/3600-3800 (FR1-N41, N78- 3GPP)
  Băng thông: 20-100MHz, IBW 100MHz
  Tốc độ (DL/UL): hỗ trợ tối đa 1.8 Gbps/380 Mbps per cell in 8T8R
  Công nghệ điều chế: QPSK, 16QAM, 64QAM, 256QAM.
  Thu phát đa ăng ten: 8T8R, 32T32R, 64T64R
  Hỗ trợ: 3GPP Release 15, 16
RRU
BBU

## Slide 18: 1. Definition
Protocol
  A set of rules or procedures for transmitting data between electronic devices
  Protocols in Transport layer: ?
Interface
  A shared boundary across which two or more components
Protocol Stack
  A set of protocols used in communication network --- ?

## Slide 19: Transmission

## Slide 20: 2. gNodeB Interfaces
Uu Interface or Radio Interface
  interface between UE and 5G gNodeB
Ng Interface or N2 Interface
  Interface between gNodeB and 5G Core network
    Ng-C interface for control plane
    Ng-U interface for user plane
  Ref: from TS 38.401 to TS 38.414
Xn Interface
  Interface between gNodeb and gNodeB
    Xn-C interface for control plane
    Xn-U interface for user plane
  Ref: from TS 38.420 to TS 38.424

## Slide 21: 3. gNodeB Protocol Stack - Control plane

## Slide 22: 4. gNodeB Protocol Stack - User plane

## Slide 23: 4. Student work
Show the gNodeB Protocol Stack for Xn Interface – Control Plane & User Plane
5 minutes

## Slide 24
5G GNODEB ARCHITECTURE & SW PROTOCOL STRUCTURE
GNODEB ARCHITECTURE
GNODEB SOFTWARE PROTOCOL
Where is the interface NG-C ?
24

## Slide 25: 5. 5G NR Layer 3
Protocol
  Radio Resource Control - RRC
  Ng Application Protocol – NgAP
  Xn Application Protocol – XnAP
  F1 Application Protocol – F1AP
Main function
  Broadcast of system information
  Manage RRC connection (establish, maintain, release)
  Manage Data Radio Bearer – DRB (establish, configuration, maintain, release)
  Mobility function & QoS management
  Manage the procedures between gNB and 5GC
  Manage the procedures among gNBs

## Slide 26: 6. 5G NR Layer 2
Service Data Application Protocol - SDAP
Package Data Convengence Protocol – PDCP
  Sequence numbering
  Ciphering & integrity
  Header compression
Radio Link Control – RLC
  3 mode of transfer: UM, AM, TM
  Segmentation and re-segmentation
  Error correction through ARQ
Medium Access Control – MAC
  Mapping logical-transport channels
  Multiplexing/ de-multiplexing.
  Scheduling
  Error correction through HARQ

## Slide 27: 7. 5G NR Layer 1

## Slide 28: 8. Channel mapping
MIB (RRC messages) - ~ 24bit
  RLC mode: TM
  Logical channel: BCCH
  Transport channel: BCH
  Physical channel: PBCH
    576 Resource Elements (240*2 + 48*2)
    Coding: polar coding
    Modulation: QPSK
    antenna transmission scheme: single
MIB message

## Slide 29
III. 5G NR Paging Feature

## Slide 30: III. 5G NR Paging Feature
1. What - Requirement
2. Paging Call Flow
3. 3GPP – document
4. Paging Occasion
5. Calculate the Paging Occasion at UE
6. Select the best Paging Occasion at gNB
7. Simulation
8. Mini-project

## Slide 31: 1. What - Requirement
Purpose of Paging Procedure:
  Triggering mobile terminated connections setup (RRC Setup Request/ RRC Resume Request)
  Informing UE of the System Information Modification
  Notifying UE of incoming ETWS/CMAS message
NGAP Paging
RRC Paging
AMF
TA1
TA2
Notes: - ETWS: Earthquake and Tsunami Warning System - CMAS: Commercial Mobile Alert System

## Slide 32: 2. Paging Call Flow
UE
gNB
AMF
Paging Occasion
Paging Occasion
PDCCH with P-RNTI
RRC Setup Request
(CCCH/UL-SCH/PUSCH)
Random Access Procedure
RRC Setup
(CCCH/DL-SCH/PDSCH)
RRC Setup Complete
(DCCH/UL-SCH/PUSCH)
NGAP: Initial UE Message / Service Request
T3513
Start
T3513
Stop
DRX Cycle
RRC: Paging
(PCCH/PCH/PDSCH)
NgAP Paging

## Slide 33: 3. 3GPP – Paging document
TS 38.331 | 5G; NR; Radio Resource Control (RRC); Protocol specification | RRC Paging Procedure
TS 38.413 | 5G; NG-RAN; NG Application Protocol (NGAP) | NGAP Paging Procedure
TS 38.423 | 5G; NG-RAN; Xn Application Protocol (XnAP) | XnAP Paging Procedure
TS 38.304 | 5G; NR; User Equipment (UE) procedures in idle mode and in RRC Inactive state | Discontinuous Reception for paging
TS 38.213 | 5G; NR; Physical layer procedures for control | PDCCH Paging Search Space

## Slide 34: 3. 3GPP – NgAP Paging message
NGAP: Paging <TS 38.413> |  |  |  | 
UE Paging Identity (Mandatory) | 5G-S-TMSI |  | AMF Set ID & AMF Pointer & 5G-TMSI | 
Paging DRX | 32, 64, 128, 256 |  |  | 
TAI List for Paging (Mandatory) | SEQUENCE {1 to 16 instances} |  |  | 
 | Tracking Area ID |  | PLMN Id & Tracking Area Code (TAC) | 
Paging Priority | 1, 2, 3, 4, 5, 6, 7, 8 |  |  | 
UE Radio Capability for Paging | Capability for NR | List of Supported NR Bands | List of Supported NR Bands | SEQUENCE {1 to 1024 instance}
 |  |  |  | 1-1024
 | Capability for E-UTRA | List of Supported E-UTRA Bands | List of Supported E-UTRA Bands | SEQUENCE {1 to 64 instance}
 |  |  |  | 1-256
Assistance Data for Paging | Recommended Cells |  |  | 
 | Paging Attempt Info |  |  | 
Paging Origin | Non-3GPP |  |  | 

## Slide 35: 3. 3GPP – RRC Paging message
RRC Paging <3GPP TS 38.331> |  |  |  | 
Paging Record List | SEQUENCE {1 to 32 instances} |  |  | 
 | PagingRecord | ue-Identity | CHOICE | 
 |  |  | ng-5G-S-TMSI | Full I-RNTI
 |  |  | BIT STRING {48 bit} | BIT STRING {40 bit}
 |  | accessType | non3GPP | 

## Slide 36: 4. Paging Occasion
Paging Occasion (PO)
  A Subframe when UE switch to active mode to check for Paging message
Paging Frame (PF)
  A Radio Frame may contain one or multiple PO(s)
DRX Cycle
  Period between two Paging Occasion (UE sleep mode duration)
0
1
2
3
4
5
6
7
8
.
.
.
28
29
30
31
32
33
34
35
36
…
…
0
1
12
13
…
0
1
12
13
PO
PO
PF
PF
DRX Cycle

## Slide 37: 5. Calculate the Paging Occasion at UE
According to 3GPP TS 38.304:
Paging Frame:
(SFN + PF_offset) mod T = (T div N)*(UE_ID mod N)
Paging Occasion:
i_s = floor (UE_ID/N) mod Ns
  T: DRX cycle of the UE
  N: Number of total paging frames in T
  Ns: number of paging occasions for a PF
  PF_offset: offset used for PF determination
  UE_ID: 5G-S-TMSI mod 1024
  Note: All Parameters except for UE_ID are signaled in SIB1.

## Slide 38: 6. Example: calculation the PF/PO at UE
SIB1
Paging
PF/PO of this UE ???

## Slide 39: 7. Example- Select the best Paging Occasion at gNB
gNodeB receives the NgAP Paging message
  At current gNB_SFN : 100 // [0-1023]
  5G-S-TMSI:
PF/PO that gNodeB Should be sent to this UE ???

## Slide 40
Mini-project

## Slide 41: 1. Exercise 1

## Slide 42: 2. Exercise 2

## Slide 43: 2. Exercise 2

## Slide 44: 3. Exercise 3

## Slide 45: 3. Note

## Slide 46
THANK YOU

## Slide 47: 3GPP release

## Slide 48: 8. 3GPP Release
TS 38.201 | NR; Physical layer; General description
TS 38.202 | NR; Services provided by the physical layer
TS 38.211 | NR; Physical channels and modulation
TS 38.212 | NR; Multiplexing and channel coding
TS 38.213 | NR; Physical layer procedures for control
TS 38.214 | NR; Physical layer procedures for data
TS 38.215 | NR; Physical layer measurements
TS 38.321 | NR; Medium Access Control (MAC) protocol specification
TS 38.322 | NR; Radio Link Control (RLC) protocol specification
TS 38.323 | NR; Packet Data Convergence Protocol (PDCP) specification
TS 38.331 | NR; Radio Resource Control (RRC); Protocol specification
TS 38.340 | NR; Adaptation layer (SDAP)
TS 38.401 | NG-RAN; Architecture description
TS 38.410 | NG-RAN; NG general aspects and principles
TS 38.411 | NG-RAN; NG layer 1
TS 38.412 | NG-RAN; NG signalling transport
TS 38.413 | NG-RAN; NG Application Protocol (NGAP)
TS 38.414 | NG-RAN; NG data transport
TS 38.415 | NG-RAN; PDU Session User Plane protocol
TS 38.420 | NG-RAN; Xn general aspects and principles
TS 38.421 | NG-RAN; Xn layer 1
TS 38.422 | NG-RAN; Xn signalling transport
TS 38.423 | NG-RAN; Xn Application Protocol (XnAP)
TS 38.424 | NG-RAN; Xn data transport
TS 38.425 | NG-RAN; NR user plane protocol
TS 38.455 | NG-RAN; NR Positioning Protocol A (NRPPa)
TS 38.460 | NG-RAN; E1 general aspects and principles
TS 38.461 | NG-RAN; E1 layer 1
TS 38.462 | NG-RAN; E1 signalling transport
TS 38.463 | NG-RAN; E1 Application Protocol (E1AP)
TS 38.470 | NG-RAN; F1 general aspects and principles
TS 38.471 | NG-RAN; F1 layer 1
TS 38.472 | NG-RAN; F1 signalling transport
TS 38.473 | NG-RAN; F1 Application Protocol (F1AP)
TS 38.474 | NG-RAN; F1 data transport
TS 38.475 | NG-RAN; F1 interface user plane protocol
TS 38.141-1 | NR; Base Station (BS) conformance testing Part 1: Conducted conformance testing
TS 38.141-2 | NR; Base Station (BS) conformance testing Part 2: Radiated conformance testing
TR 38.810 | NR; Study on test methods
TS 38.133 | NR; Requirements for support of radio resource management
TS 38.104 | NR; Base Station (BS) radio transmission and reception